## Slide 1: EE 542: Lab 3, UDP Reliable File Transfer
Sufyan Shaikh & Charlie André

## Slide 2: The Task
Using a link speed of 100 Mbps
Vary loss and Delay
Create a robust file transfer protocol using UDP
Achieve at least 20% link utilization (20Mbps)

## Slide 3: The Solution (in words)
Send UDP packets of size less than the MTU
Receiver tells the sender which packets were missed using a NACK linked list
Sender resends each missed packet multiple times
This repeats until the receiver has received all of the packets

## Slide 4: The Solution as a diagram
Sender
Receiver
Sends the entire file in UDP packets
Replies with the packets that were missed
Repeats while there are still dropped packets
Bind
Socket Creation
Socket Creation
CLOSE
CLOSE
Receive files and send nacks of packets dropped
Receive files and send nacks of packets dropped

## Slide 5: Results Table
Delay (ms) | Added Loss (percent loss) | Data Rate (Mbps)
0 | 0 | 47.817
10 | 1 | 39.018
200 | 20 | 46.841

## Slide 6: Lessons Learned
TCP does not work for lossy links with long delay
Crafty techniques are required for lossy links
UDP bypasses the need for a handshake on each packet
Use of NACK is required to resend the packets that were missed